## Slide 1: Introduction
What is Computer Graphics?
Applications
Graphics packages

## Slide 2: What is Computer Graphics?
Creation, Manipulation and Storage of geometric objects (modeling) & their images (rendering)
Display those images on screens or hardcopy devices

## Slide 3: Applications of Computer Graphics
Computer Aided Design (CAD)
Presentation Graphics
Computer Art
Entertainment (animation, games, …)
Education & Training
Visualization (scientific & business)
Image Processing
Graphical User Interfaces

## Slide 4: 1.Computer Aided Design (CAD)
  Used in design of buildings, automobiles, aircraft, watercraft, spacecraft, computers, textiles & many other products
  Objects are displayed in wire frame outline form
  Software packages provide multi-window environment

## Slide 5
Graphics design package provides standard shapes (useful for repeated placements)
Animations are also used in CAD applications
Realistic displays of architectural design permits simulated “walk” through the rooms (virtual -reality systems)

## Slide 6: 2.Presentation Graphics
Used to produce illustrations for reports or generate slides for use with projectors
Commonly used to summarize financial, statistical, mathematical, scientific, economic data for research reports, managerial reports & customer information bulletins
Examples : Bar charts, line graphs, pie charts, surface graphs, time chart

## Slide 7: Examples of presentation graphics

## Slide 8: Examples of presentation graphics

## Slide 9: 3.Computer Art
Used in fine art & commercial art
  Includes artist’s paintbrush programs, paint packages, CAD packages and animation packages
  These packages provides facilities for designing object shapes & specifying object motions.
  Examples : Cartoon drawing, paintings, product advertisements, logo design

## Slide 10: Examples :

## Slide 11: Computer Art
Electronic painting
  Picture painted electronically on
  a graphics tablet (digitizer) using a stylus
  Cordless, pressure sensitive stylus
Morphing
  A graphics method in which one object is transformed into another

## Slide 13: 4.Entertainment
Movie Industry
  Used in motion pictures, music
  videos, and television shows.
  Used in making of cartoon
  animation films
Slide information from Leonard McMillian's slides
http://www.cs.unc.edu/~mcmillan/comp136/Lecture1/compgraf.html

## Slide 14: Computer Graphics is about animation (films)

## Slide 15
Game Industry
  Focus on interactivity
  Cost effective solutions
  Avoiding computations and
  other tricks

## Slide 16: 5.Education & Training
Computer generated models of physical, financial and economic systems are used as educational aids.
Models of physical systems, physiological systems, population trends, or equipment such as color-coded diagram help trainees understand the operation of the system

## Slide 17
Specialized systems used for training applications
  simulators for practice sessions or training of ship captains
  aircraft pilots
  heavy equipment operators
  air traffic-control personnel

## Slide 18: Training

## Slide 19: 6.Visualization
Scientific Visualization
  Producing graphical representations for scientific, engineering, and medical data sets

## Slide 20: Scientific Visualisation
To view below and above our visual range

## Slide 21
Business Visualization is used in connection with data sets related to commerce, industry and other non-scientific areas
Techniques used- color coding, contour plots, graphs, charts, surface renderings & visualizations of volume interiors.
Image processing techniques are combined with computer graphics to produce many of the data visualizations

## Slide 22: 7. Image Processing
CG- Computer is used to create a picture
Image Processing – applies techniques to modify or interpret existing pictures such as photographs and TV scans
Medical applications
  Picture enhancements
  Tomography
  Simulations of operations
  Ultrasonics & nuclear medicine scanners
2 applications of image processing
  Improving picture quality
  Machine perception of visual information (Robotics)

## Slide 23
To apply image processing methods
  Digitize a photograph (or picture) into an image file
  Apply digital methods to rearrange picture parts to
    enhance color separations
    Improve quality of shading
  Tomography – technique of X-ray photography that allows cross-sectional views of physiological systems to be displayed
  Computed X-ray tomography (CT) and position emission tomography ( PET) use projection methods to reconstruct cross sections from digital data
  Computer-Aided Surgery is a medical application technique to model and study physical functions to design artificial limbs and to plan & practice surgery

## Slide 25: 8.Graphical User Interfaces
Major component – Window manager (multiple-window areas)
To make a particular window active, click in that window (using an interactive pointing device)
Interfaces display – menus & icons
Icons – graphical symbol designed to look like the processing option it represents
Advantages of icons – less screen space, easily understood
Menus contain lists of textual descriptions & icons

## Slide 27: Graphics packages
A set of libraries that provide programmatically access to some kind of graphics 2D functions.
Types
  GKS-Graphics Kernel System – first graphics package – accepted by ISO & ANSI
  PHIGS (Programmer’s Hierarchical Interactive Graphics Standard)-accepted by ISO & ANSI
  PHIGS + (Expanded package)
  Silicon Graphics GL (Graphics Library)
  Open GL
  Pixar Render Man interface
  Postscript interpreters
  Painting, drawing, design packages

## Slide 28: Display Devices

## Slide 29: Displays
Emissive display -- convert electrical energy into light
- Cathode ray tube (CRT)
- Flat panel CRT
- Plasma panels (gas-discharge display)
- Thin-film electroluminescent (EL) display
- Light-emitting diodes
Non-Emissive display -- optical effect: convert sunlight or light from other source into graphic patterns.
- Liquid-crystal device (LCD) – flat panel
- Passive-matrix LCD
- Active-matrix LCD

## Slide 30: Monochrome Cathode Ray Tube (CRT)
Cathode Ray – beam of electrons
- emitted by an electron gun
- accelerated by a high positive voltage near the face of the tube
- forced into a narrow stream by a focusing system
- directed toward a point on the screen by the magnetic field generated
by the deflection coils
- hit onto the the phosphor-coated screen
- phosphor emits visible light, whose intensity depends on the number of
electrons striking on the screen
Cathode
Focusing
system
Horizontal
& vertical
deflection
Electron gun

## Slide 31: Properties of the CRT
Phosphor Persistence (PP)
- the light output decays exponentially with time.
- a phosphor’s persistence is defined as the time from the removal of
excitation to the moment of decaying the light to one-tenth of its
original intensity
- low persistence -> good for animation
- high persistence -> good for static picture with high complexity
- typical range: 10ms – 60ms
Refresh rate (RR)
- number of times per second the image is redrawn (e.g., 60 or higher)
Critical fusion frequency (CFF)
- the refresh rate above which a picture stops flickering and becomes
steady
longer PP -> lower CFF required
Notes: Ms (millisecond – 1 one thousands of a second)

## Slide 32: Properties of the CRT
Resolution
- the maximum number of points that can be displayed without overlap on a CRT
- high-definition system, e.g. 1280 * 1024 pixels
- resolution depends on the type of phosphor, the intensity to be
displayed, focusing and deflection systems, size of video memory
Horizontal scan rate
- the number of scan lines per second that the CRT is able to display
- refresh rate * number of scan lines per frame

## Slide 33: CRT Color Monitor

## Slide 34: Beam Penetration method
This technique is used with random scan monitors.
In this technique inside of CRT coated with two phosphor layers usually red and green.
The outer layer of red and inner layer of green phosphor.
The color depends on how far the electron beam penetrates into the phosphor layer.

## Slide 35
A beam of fast electron penetrates more and excites inner green layer while slow electron excites outer red layer.
At intermediate beam speed we can produce combination of red and green lights which emit additional two colors orange and yellow.
The beam acceleration voltage controls the speed of the electrons and hence color of pixel.

## Slide 36: Shadow Mask
•Shadow mask has one small hole for each phosphor triad.
•Holes are precisely aligned with respect to both the triads and the electron guns, so that each dot is exposed to electrons from only one gun.
•The number of electrons in each beam controls the amount of red, blue and green light generated by the triad.

## Slide 37
Sr. No. | Basis | Beam Penetration | Shadow Mask
1. | Colors produced | In this method, there is the production of only four colors i.e., red, green, yellow, orange. | In this method, there is the production of millions of colors.
2. | Color dependency | As in this method only four colors are produced it is because of the speed of the electron gun. | As in this method millions of colors are produced because it depends upon the intensity value of the three available guns.
3. | Number of electron guns used. | In this method, only one electron gun is used. | In this methods, three electron guns are used; i.e red, green and blue.
4. | Picture quality | As we know in this different colors and shades are not possible. So, it’s picture quality is poor. | As we know in this different colors and shades are possible. So, it’s picture quality is quite good.
5. | Realistic view | This method is not suitable for providing the realistic view. | This method is suitable for providing the realistic view.
6. | Resolution | This method provides high resolution. | Whereas, this method does not able to provide high resolution.
7. | Cost | It is cheaper than shadow mask method. | It is an expensive method.
8. | Application | It is used in random scan system to display color. | It is used in raster scan system to display color.

## Slide 38: Properties of the CRT
Dot Pitch –the spacing between pixels on a CRT, measured in millimeters. Generally, the lower the number, the more detailed the image.
Notes: Many manufacturers and retailers tend to not list the dot pitch ratings anymore. This rating refers to the size of a given pixel on the screen in millimeters. This tended to be a problem in past years as screens that attempted to do high resolutions with large dot pitch ratings tended to have a fuzzy image because of the color bleeding between pixels on the screen. Lower dot pitch ratings are preferred as it gives the display greater image clarity. Most ratings for this will be between .21 and .28 mm with most screens having an average rating of about .25 mm.

## Slide 39: Output Scan Technology
Vector display
- line drawing and stroke drawing in a random order
Raster display
- horizontal scan line order

## Slide 40: Vector Display
Vector display (1960s)
- vector system consists of:
display processor (controller),
display buffer memory
CRT
- The buffer stores the computer-produced display list or display program
- Display program contains point- and point-plotting commands with (x, y, z)
endpoint coordinates
- The commands for plotting are interpreted by the display processor
- The principle of vector system is random scan
The beam is deflected from endpoint to endpoint, as dictated by the order of the
display command
- display list needed to be refreshed (e.g., 30Hz)

## Slide 41: Vector Display
Vector display (1960s)
:
:
Move
10
15
LINE
300
400
CHAR
Lu
cy
LINE
:
:
JMP
Display Controller (DC)
Monitor
Lucy
Host Computer
display buffer

## Slide 42: Raster Display
Raster display (since 1970s)
- Raster system consists of:
display processor (input, refreshing, scan converting)
video controller
buffer memory (frame buffer)
CRT
- The buffer stores the primitive pixels, rather than display list or display program
- Video controller reads the pixel contents to produce the actual image on the
screen
- The image is represented as a set of raster scan lines, and forms a matrix of pixels.
- need refresh the raster display (e.g., 60Hz)

## Slide 43: Architecture of a simple raster-graphics system

## Slide 44: Architecture of a raster system
with a fixed portion of the system memory reserved for the frame buffer.

## Slide 45: Basic video-controller refresh operations

## Slide 46: Architecture of a raster-graphics system with a display processor.

## Slide 47: BASIC DEFINITIONS
RASTER: A rectangular array of points or dots.
PIXEL (Pel): One dot or picture element of the raster
SCAN LINE: A row of pixels
Video raster devices display an image by sequentially drawing out the pixels of the scan lines that form the raster.

## Slide 48: Raster Display
Raster scan with blanked retrace
Scan line
Vertical retrace
Horizontal retrace

## Slide 49: Scanning An Image
Frame: The image to be scanned out on the CRT.
•Some minimum number of frames must be redisplayed (or refreshed) each second to eliminate flicker in the image.
•Critical Fusion Frequency --The refresh rate above which a picture stops flickering and fuses into a steady image is called the critical fusion frequency.
Typically 60 times per second for raster displays.
•Varies with intensity, individuals, phosphor persistence, room lighting.

## Slide 50: Video Controller
Access the frame buffer to refresh the screen
Control the operation for display
Color look-up table
Linear
address
X
address
Y
address
Raster-scan
generator
Frame
buffer
Pixel
values
Horizontal
& vertical
Deflection signal
Data
Intensity
or color

## Slide 51: Video Controller
Types of refresh
Interlaced (mostly for TV for reducing flickering effect -- NTSC)
- two fields for one frame
- odd-field: odd-numbered scan lines
- even-field: even-numbered scan lines
- refresh rate: e.g., NTSC: 60Hz (60 fields per second); 30 frame/s.
PAL: 50Hz
Non-interlaced (mostly for monitor)
- refresh rate: e.g., 60Hz or more
Odd-field
Even-field
Notes: PAL –Short for Phase Alternating Line, the dominant television standard in Europe. The United States uses a different standard, NTSC. Whereas NTSC delivers 525 lines of resolution at 60 half-frames per second, PAL delivers 625 lines at 50 half-frames per second. Many video adapters that enable computer monitors to be used as television screens support both NTSC and PAL signals.
(Phase Alternating Line) A color TV standard that was developed in Germany. It broadcasts 25 interlaced frames per second (50 half frames per second) at 625 lines of resolution. Brazil uses PAL M, which broadcasts 30 fps. PAL is used throughout Europe and China as well as in various African, South American and Middle Eastern countries. PAL's color signals are maintained automatically, and the TV set does not have a user-adjustable hue control. See NTSC and SECAM.
NTSC –Short for National Television System Committee. The NTSC is responsible for setting television and video standards in the United States (in Europe and the rest of the world, the dominant television standards are PAL and SECAM). The NTSC standard for television defines a composite video signal with a refresh rate of 60 half-frames (interlaced) per second. Each frame contains 525 lines and can contain 16 million different colors. The NTSC standard is incompatible with most computer video standards, which generally use RGB video signals. However, you can insert special video adapters into your computer that convert NTSC signals into computer video signals and vice versa.
(National TV Standards Committee) A color TV standard that was developed in the U.S. Administered by the FCC, NTSC broadcasts 30 interlaced frames per second (60 half frames per second, or 60 "fields" per second in TV jargon) at 525 lines of resolution. The signal is a composite of red, green and blue and includes an audio FM frequency and an MTS signal for stereo. NTSC is used throughout the world, including the U.S., Canada, Japan, South Korea and several Central and South American countries. See PAL, SECAM and ATSC.
SECAM –(Systeme En Couleur Avec Memoire) A color TV standard that was developed in France. It broadcasts 25 interlaced frames per second (50 half frames per second) at 625 lines of resolution. SECAM is used in France and Russia and many countries in Africa, Eastern Europe and the Middle East. See NTSC and PAL.

## Slide 52: Display Processor
Also called either a Graphics Controller or Display CoProcessor
Specialized hardware to assist in scan converting output primitives into the frame buffer.
Fundamental difference among display systems is how much the display processor does versus how much must be done by the graphics subroutine package executing on the general-purpose CPU.

## Slide 53: Frame Buffer
A frame buffer may be thought of as computer memory organized as a two-dimensional array with each (x,y) addressable location corresponding to one pixel.
Bit Planes or Bit Depth is the number of bits corresponding to each pixel.
A typical frame buffer resolution might be
640 x 480 x 8
1280 x 1024 x 8
1280 x 1024 x 24

## Slide 54: 1-Bit Memory. Monochrome Display (Bit-map Display)
Notes: (1280 X 1024 X1) = 163840 bytes or 160 KB

## Slide 55: 3-Bit Color Display
3
red
green
blue
COLOR: black red green blue yellow cyan magenta white
R
G
B
0
0
0
1
0
0
0
1
0
0
0
1
1
1
0
0
1
1
1
0
1
1
1
1
Notes: (1280 X 1024 X 3)/8 = 480 KB

## Slide 56: True Color Display 24 bitplanes, 8 bits per color gun. 224 = 16,777,216 colors
Green
Red
Blue
8
8
8
Notes: (1280 X 1024 X 24 ) = 3,840 KB or 3,932,160 bytes

## Slide 57: Difference between raster scan and random scan
Base of Difference | Raster Scan System | Random Scan System
Electron Beam | The electron beam is swept across the screen, one row at a time, from top to bottom. | The electron beam is directed only to the parts of screen where a picture is to be drawn.
Resolution | Its resolution is poor because raster system in contrast produces zigzag lines that are plotted as discrete point sets. | Its resolution is good because this system produces smooth lines drawings because CRT beam directly follows the line path.
Picture Definition | Picture definition is stored as a set of intensity values for all screen points, called pixels in a refresh buffer area. | Picture definition is stored as a set of line drawing instructions in a display file.
Realistic Display | The capability of this system to store intensity values for pixel makes it well suited for the realistic display of scenes contain shadow and color pattern. | These systems are designed for line- drawing and can’t display realistic shaded scenes.
Draw an Image | Screen points/pixels are used to draw an image. | Mathematical functions are used to draw an image.

## Slide 58: Interlaced Systems
In some raster system interlacing technique is used for painting the screen . Instead of refreshing every line in an interlaced mode the electron gun sweeps alternate line in each pass (each frame is displayed in two frames odd numbered being refreshed first and then the even numbered lines.).
* This is an effective
technique for avoiding flicker

## Slide 59: Direct View Storage Tube
In all the earlier technologies we need refreshing of the screen
An alternative method is Direct View Storage Tube .It stores the picture information as a charge distribution just behind the phosphor coated screen.
Two electron guns primary gun and flood gun are used
Primary gun stores the picture pattern and flood gun maintains the picture display

## Slide 60: DVST Vs Refresh CRT
In DVST since no refreshing required so complex pictures can be displayed at higher resolution without flicker.
However DVST ordinarily does not display colors and parts of image cannot be erased here so not good for animation